PCIe Dual-Port Gigabit Network Card

MC-PCIE-712

User Manual

Ver. 1.00

All brand names and trademarks are properties of their

Respective owners.

Product Introduction

It is provide two RJ45 port and support 10/100/1000M rate full duplex, half-duplex adaptive. It is support to send Gigabit super-long frame ,highest can provide two-way data transfer rate of 1000M .Using it can be implement gigabit network to the desktop ,Enhance network performance .It is 100 times faster than, and yet 100% fully backward compatible with 10/100BASE-T system, therefore, it can be easily plugged into almost any existing network with CAT-5 cabling.

Features & Specification

- Complies with PCI-Express Revision 1.1

- PCI-Express 1-Lane (x1) interface

- Supports standard and low profile chassis

- A high performance 1000BASE-T Ethernet controller card

- Backward compatible to 10/100BASE-T networking

- Supports jumbo frame to 9K bytes

- 10/100/1000Mbps data rate auto negotiation operation

- Compatible to existing CAT-5 UTP cabling

- Fully compliant with IEEE802.3,IEEE802.3u, IEEE802.3ab

- Supports half / full duplex mode and 802.3x Flow Control

- Supports IEEE802.1P Layer2 Priority Encoding

- Supports IEEE 802.1Q VLAN tagging

- Transmit /Receive on-chip buffer support

- Crossover Detection and Auto Correction operation

- Supports power down/link down power saving

- Wake-on-LAN and remote wake-up function support

- 2 * RJ45 Gigabit lan ports

System Requirements

Windows® 98se/me/2000/XP/2003/Vista /Win7/2008/Win8/Win8.1/Win10 (32/64 bit)

PCI Express-enabled system with an available PCI Express slot

Package Contents

1 x PCIe Dual Port Gigabit Network Card

1 x User Manual

1 x Driver CD

Driver Installation

1. Please insert the CD driver bound into your CD-ROM Drive.

2. At the Windows desktop, click Start, Run.

3. 1 For Windows® WIN98SE,WinME (32/64 bit)

Type“RTL8168,RTL8111C,RTL8111E\Windows\WIN98SE,WINME\PCIE_Install_5708_1119\setup. exe”, Double click it.

3. 2 For Windows® WIN2K, XP, Server 2003 (32/64 bit)

Type“RTL8168,RTL8111C,RTL8111E\Windows\WIN2K,XP,2003\PCIE_Install_5790_11182011\setup.exe”, Double click it.

3. 3 For Windows® Vista, WIN2008 (32/64 bit)

Type“RTL8168,RTL8111C,RTL8111E\Windows\VISTA,WIN2008\Install_Vista_6250_11182011\setup.exe”, Double click it.

3.4 For Windows® Win7, WIN2008 (32/64 bit)

Type“RTL8168,RTL8111C,RTL8111E\Windows\WIN7,WIN2008\Install_Win7_7049_11182011\setup.exe”, Double click it.

3.5 For Windows® Win8, Win8.1 (32/64 bit)

Type“RTL8168,RTL8111C,RTL8111E\Windows\Win8,Win8.1\Install_Win8_8.1_8020_09182013\setup.exe”, Double click it.

3.6 For Windows® Win10 (32/64 bit)

Type

“RTL8168,RTL8111C,RTL8111E\Windows\Win10\Install_Win10_10003_08202015\setup.exe”, Double click it.

4. Follow the on-screen instructions to complete the installation.

Support:

If you have further questions, please contact our customer support and you can find more information on our homepage: